H8/H89 I/O Port Assignments
May 28, 2021

NOTE: Some boards can be configured for any/many port ranges, however available software may not support all ranges. Unless otherwise indicated by “*”, boards are shown in the port ranges required/expected by software.

Software is not able to detect port ranges of hardware. The dipswitches at port 362Q allow for software detection of the configuration of port ranges 170Q and 174Q only. Zx80 CPU boards V4 and later allow for extended port configuration for ranges 270Q and 274Q for certain devices. With the exception of H67 and H47 devices, software tends to hard-code the port ranges.

TBD(4)	HA-8-2 ADC/DAC

000Q	512K MMU	ECS PC-12 CARD
001Q	512K MMU	ECS PC-12 CARD
002Q	512K MMU	ECS PC-12 CARD
003Q	512K MMU	ECS PC-12 CARD
004Q	512K MMU	ECS PC-12 CARD
005Q	512K MMU	ECS PC-12 CARD
006Q	512K MMU	ECS PC-12 CARD
007Q	512K MMU	ECS PC-12 CARD
010Q		ECS PC-12 CARD
011Q		ECS PC-12 CARD
012Q		ECS PC-12 CARD
013Q		ECS PC-12 CARD
014Q		ECS PC-12 CARD
015Q		ECS PC-12 CARD
016Q		ECS PC-12 CARD
017Q		ECS PC-12 CARD
020Q		ECS PC-12 CARD
021Q		ECS PC-12 CARD
022Q		ECS PC-12 CARD
023Q		ECS PC-12 CARD
024Q
025Q
026Q
027Q
030Q	82C55 CARD *H
031Q	82C55 CARD *H
032Q	82C55 CARD *H
033Q	82C55 CARD *H
034Q	82C55 CARD *G
035Q	82C55 CARD *G
036Q	82C55 CARD *G
037Q	82C55 CARD *G
040Q
041Q
042Q
043Q
044Q	82C55 CARD *F
045Q	82C55 CARD *F
046Q	82C55 CARD *F
047Q	82C55 CARD *F
050Q	82C55 CARD *E
051Q	82C55 CARD *E
052Q	82C55 CARD *E
053Q	82C55 CARD *E
054Q	82C55 CARD *D
055Q	82C55 CARD *D
056Q	82C55 CARD *D
057Q	82C55 CARD *D
060Q	82C55 CARD *C
061Q	82C55 CARD *C
062Q	82C55 CARD *C
063Q	82C55 CARD *C
064Q
065Q
066Q
067Q
070Q	82C55 CARD *B
071Q	82C55 CARD *B
072Q	82C55 CARD *B
073Q	82C55 CARD *B
074Q
075Q
076Q
077Q	TRIONYX Z-H8 CTL PORT
100Q	H8xSPI (WIZNET/SDCard)
101Q	H8xSPI (WIZNET/SDCard)
102-167Q	--unused--
170Q	H37	H67 *1	H47 *1
171Q	H37	H67 *1	H47 *1
172Q	H37	H67 *1	H47 *1
173Q	H37	H67 *1	H47 *1
174Q	H17	H67 *2	H47 *2
175Q	H17	H67 *2	H47 *2
176Q	H17	H67 *2	H47 *2
177Q	H17	H67 *2	H47 *2
200Q	H8-Z80-64 GIDE	H8_DUAL_GIDE	H8-AM9511-APU
201Q	H8-Z80-64 GIDE	H8_DUAL_GIDE	H8-AM9511-APU
202Q	H8-Z80-64 GIDE	H8_DUAL_GIDE	H8-AM9511-APU
203Q	H8-Z80-64 GIDE	H8_DUAL_GIDE	H8-AM9511-APU
204Q	H8-Z80-64 GIDE	H8_DUAL_GIDE
205Q	H8-Z80-64 GIDE	H8_DUAL_GIDE
206Q	H8-Z80-64 GIDE	H8_DUAL_GIDE
207Q	H8-Z80-64 GIDE	H8_DUAL_GIDE
210Q	H8-Z80-64 GIDE	H8_DUAL_GIDE
211Q	H8-Z80-64 GIDE	H8_DUAL_GIDE
212Q	H8-Z80-64 GIDE	H8_DUAL_GIDE
213Q	H8-Z80-64 GIDE	H8_DUAL_GIDE
214Q	H8-Z80-64 GIDE	H8_DUAL_GIDE
215Q	H8-Z80-64 GIDE	H8_DUAL_GIDE
216Q	H8-Z80-64 GIDE	H8_DUAL_GIDE
217Q	H8-Z80-64 GIDE	H8_DUAL_GIDE
220Q		H8_DUAL_GIDE	H8 SPEED BOARD
221Q		H8_DUAL_GIDE
222Q		H8_DUAL_GIDE
223Q		H8_DUAL_GIDE
224Q		H8_DUAL_GIDE
225Q		H8_DUAL_GIDE
226Q		H8_DUAL_GIDE
227Q		H8_DUAL_GIDE
230Q		H8_DUAL_GIDE
231Q		H8_DUAL_GIDE
232Q		H8_DUAL_GIDE
233Q		H8_DUAL_GIDE
234Q		H8_DUAL_GIDE
235Q		H8_DUAL_GIDE
236Q		H8_DUAL_GIDE
237Q		H8_DUAL_GIDE
240Q	RTC72421
241Q	RTC72421
242Q	RTC72421
243Q	RTC72421
244Q	RTC72421
245Q	RTC72421
246Q	RTC72421
247Q	RTC72421
250Q	RTC72421
251Q	RTC72421
252Q	RTC72421
253Q	RTC72421
254Q	RTC72421
255Q	RTC72421
256Q	RTC72421
257Q	RTC72421
260Q	H8 USB
261Q	H8 USB
262Q	H8 USB
263Q	H8 USB
264Q
265Q
266Q
267Q
270Q	H67 *3	HA-8-3 GRAPHICS CARD
271Q	H67 *3	HA-8-3 GRAPHICS CARD
272Q	H67 *3	HA-8-3 GRAPHICS CARD
273Q	H67 *3	HA-8-3 GRAPHICS CARD
274Q	H67 *4	HA-8-3 GRAPHICS CARD
275Q	H67 *4	HA-8-3 GRAPHICS CARD
276Q	H67 *4	HA-8-3 GRAPHICS CARD
277Q	H67 *4
300-317Q	--unused--
320Q	"ALT" SERIAL PORT		82C55 CARD *A
321Q	"ALT" SERIAL PORT		82C55 CARD *A
322Q	"ALT" SERIAL PORT		82C55 CARD *A
323Q	"ALT" SERIAL PORT		82C55 CARD *A
324Q	"ALT" SERIAL PORT
325Q	"ALT" SERIAL PORT
326Q	"ALT" SERIAL PORT
327Q	"ALT" SERIAL PORT
330Q	"MODEM" SERIAL PORT	VDIP1/FT245R USB
331Q	"MODEM" SERIAL PORT	VDIP1/FT245R USB
332Q	"MODEM" SERIAL PORT	VDIP1/FT245R USB
333Q	"MODEM" SERIAL PORT
334Q	"MODEM" SERIAL PORT
335Q	"MODEM" SERIAL PORT
336Q	"MODEM" SERIAL PORT
337Q	"MODEM" SERIAL PORT
340Q	"LP" SERIAL PORT
341Q	"LP" SERIAL PORT
342Q	"LP" SERIAL PORT
343Q	"LP" SERIAL PORT
344Q	"LP" SERIAL PORT
345Q	"LP" SERIAL PORT
346Q	"LP" SERIAL PORT
347Q	"LP" SERIAL PORT
350Q	"CONSOLE" SERIAL PORT
351Q	"CONSOLE" SERIAL PORT
352Q	"CONSOLE" SERIAL PORT
353Q	"CONSOLE" SERIAL PORT
354Q	"CONSOLE" SERIAL PORT
355Q	"CONSOLE" SERIAL PORT
356Q	"CONSOLE" SERIAL PORT
357Q	"CONSOLE" SERIAL PORT
360Q	H8 FRONT PANEL + CTL
361Q	H8 FRONT PANEL
362Q	H8/H89 CTL/DIPSW PORT	+ Zx80 V3/4 SPEED CONTROL
363Q		Zx80 V4 CLOCK ENABLE
364Q
365Q
366Q
367Q
370Q	H8-5 CASS SERIAL PORT	H8-2 PARALLEL CH-0
371Q	H8-5 CASS SERIAL PORT	H8-2 PARALLEL CH-0
372Q	H8-5 CONSOLE SERIAL
373Q	H8-5 CONSOLE SERIAL
374Q		H8-2 PARALLEL CH-1
375Q		H8-2 PARALLEL CH-1
376Q		H8-2 PARALLEL CH-2
377Q		H8-2 PARALLEL CH-2

*1 *2 *3 *4 – Card is configuration for alternate I/O ports.
*A..*H – Port ranges may be assigned to chips as desired. A maximum of 5 ranges can be used.